## Slide 1
Dr. Shuwen Hu
shuwen.hu@rmit.edu.au
27 Nov 2025
Predication of Daily Weight Gain with Cattle Behaviour and Daily Activity Using Triaxial Accelerometer Data

## Slide 2
Who here has a Fitbit/Apple Watch?

## Slide 3: Why Sensors on Cattle?
More reliably than a postdoc with a clipboard
Objectively
It isn’t based on someone’s opinion
Remotely
We don’t need to be there watching
Continuously
Animals can be monitored 24 / 7
Broadly
Lots of animals in typical production environments
Notes: Many important animal production traits are not easily measured at scale
-growth
-feed efficiency
-health and wellbeing
-reproduction

## Slide 4: Correlating animal behaviour to pasture intake and efficiency
Can animal behaviour be interpreted from inertial sensor signals?
Does a relationship exist between behaviours and production?
Bite size
Behaviour
Bite rate
Production
(e.g. weight)
Efficiency
Intake
Ratio
Health, Welfare

## Slide 5: The Basic eGrazor
Worn as a collar
Solar panels to recharge
Counterweight to keep it upright
Rugged cowproof case. To stop it getting smashed…but with fashionable pink colour.
Batteries
Control board

## Slide 6: What technology is in eGrazor?
LOCI2
LOCI3
LOCI4

## Slide 7: Sensors for monitoring
Location/GPS/Antenna
IMU – Acc/Gyro
Humidity/Temp/Pressure
TAURUS

## Slide 8
Fun Time at Lab

## Slide 9
Head Movement
Three-axes accelerometer

## Slide 10
Analytical Challenges
Large volume Data: 50 sample readings per second
Noisy Data
How to present data in a meaningful way?
How to associate measures to animal welfare outcomes?

## Slide 11
Activity (Motion intensity) is calculated for each 5 mins window
A first-order high-pass Butterworth filter is used to reduce noisy data and gravity effects
Activity: =
At 50 HZ, we calculated 50*60*5=1500 values for each 5 mins
We then calculate the median for each 5 mins window size
For each hour, we sum medians for each of 5 mins window size
For daily activity, we sum each hour activity for 24 hours
Activity Metric

## Slide 12: Collect synchronized annotation data
  Video
  4 corners of paddock
  GPS on camera
  GoPro
    8 hours

## Slide 13: Cattle Behaviors
Drinking
Resting
Walking
Other
Ruminating
Grazing

## Slide 14: 2022 Experiment Description
Device: eGrazor Collar
Frequency: 50 HZ
32GB micro-SD flash memory card
Location: Gatton, Queensland, Australia
Time: November 21 to December 19, 2022
Breed: 60 Brahman or Droughtmaster steers
The live weight data were collected weekly.

## Slide 15: Constrained Convolutional Neural Network
Arablouei, Reza and Bishop-Hurley, Greg and Bagnall, Neil and Ingham, Aaron, Cattle Behaviour Recognition from Accelerometer Data: Leveraging In-Situ Cross-Device Model Learning. https://www.sciencedirect.com/science/article/pii/S0168169924009372

## Slide 16: Behaviour Classification Accuracy
MCC0: 0.8891 ± 0.0010 (grazing) MCC1: 0.8573 ± 0.0082 (walking) MCC2: 0.8414 ± 0.0014 (ruminating) MCC3: 0.8455 ± 0.0012 (resting) MCC4: 0.6561 ± 0.0169 (drinking) MCC5: 0.1134 ± 0.0102 (other)
Matthews correlation coefficient (MCC): 0.8378 ± 0.0011

## Slide 17
Daily Activity
Notes: 57 animals
27 days

## Slide 18
Daily Behaviours Time Vs Daily Activity

## Slide 19: Pearson Correlations

## Slide 20: Linear Mixed Model
57 animals in total
Marginal
Conditional
is the variance of the fixed effect components
is the variance of random effects
is the “observation-level” variance.

## Slide 21: Check Multicollinearity
Variance Inflation Factor (VIF)
If VIF > 4, further investigation is required
If VIF > 10, there is significant multicollinearity that needs to be corrected.

## Slide 22: Principal Component Analysis
6 behaviours: 'grazing', 'ruminating', 'walking', 'resting’, ‘drinking’, ‘other’
6 components: PC1, PC2, PC3, PC4, PC5 and PC6
The explained variance for 6 components:
[0.489, 0.933, 0.991, 0.997, 1., 1.]
We choose 3 components as the independent variables in linear mixed model

## Slide 23: LMM with PCA

## Slide 24: PCA Results
Activity ~ 15.454 + 0.765*PC1 - 0.206*PC2 + 2.052*PC3 + 1.912*id + error
PC1 = 0.772*grazing - 0.044*ruminating - 0.051*walking -0.631*resting - 0.023*drinking - 0.023*other
PC2 = -0.346*grazing + 0.806*ruminating + 0.002*walking -0.48*resting + 0.018*other
PC3 = -0.24*grazing - 0.31*ruminating + 0.852*walking - 0.343*resting - 0.001*drinking + 0.042*other

## Slide 25: Daily Live Weight Gain
The live weight data were collected weekly.
The average daily weight gain is calculated for each animal.
The aim is to use the sensor-based features (daily behavior time and daily activity) to predict daily weight gain.
Weather information include Minimum and Maximum Temperature, Rainfall and Wind Speed
Five-fold cross validation using machine learning algorithm

## Slide 26: Predictions for daily weight gain
 | RMSE | R-squared
Linear Regression | 0.8668 | 0.4667
Decision Tree | 1.0866 | 0.0950
Random Forest | 0.8705 | 0.4703
Support Vector Regression | 1.1155 | 0.1480
XG Boost | 0.8984 | 0.4359
Neural Network | 0.8834 | 0.4431
100 repeats

## Slide 27: Take Home Messages
On-animal sensors such as accelerometers have been widely and successfully used to classify cattle behaviours.
Accelerometers are used to collect high-frequency data on activity of animals in real-time.
Different behaviours would cause different movements and further need different energy budgets.
Grazing and walking are positively correlated with activity scores, whereas ruminating and resting are negatively correlated with activity scores.
The liveweight gain could not be fully explained by measurements taken in this study, but we showed how these factors can influence the variability in cattle performance.

## Slide 28: Acknowledgement